M.TECH. DEGREE EXAMINATION

Branch : Electrical and Electronics Engineering

Specialization – Power Electronics

Model Question Paper - II

Second Semester

MEEPE 204  MODELING AND ANALYSIS OF ELECTRICAL MACHINES.

(Regular – 2011Admission onwards)

Time: Three hours                                  					Max. Marks: 100

Answer all questions

I (a) 	Derive the energy balance equation in an electromechanical energy conversion device.                               					 		[10 Marks]

(b)     Derive the expressions for stored magnetic energy and co-energy in a singly excited system.								 [15 Marks]

OR

(c)	Derive the expressions for stored magnetic energy and electromagnetic torque in the case of a doubly excited system.					 [25 Marks]

II 	Derive the self and mutual inductances of a 2-pole, 3-phase Y-connected, symmetrical synchronous machine. 					[25 Marks]

OR

Derive the self and mutual inductances of a 2-pole, 3-phase Y- connected symmetrical induction machine.						 [25 Marks]

III	For a 2-pole, 3-phase Y-connected symmetrical induction machine, derive voltage and torque equations in machine variables. 			[25 Marks]

OR

- Write short notes on :

Reference-frame theory, and

Commonly used reference frames.					  [10 Marks]

- Derive the stator reference frame model of an induction machine.

[15 Marks]

IV 		Draw the equivalent circuits of a 3-phase synchronous machine using voltage  equations in rotor reference- frame variables. 				[25 Marks]

OR

(a) 	For a 2-phase unsymmetrical induction machine, derive the voltage equation in machine variables. 								[15 Marks]

(b)   Draw and explain the equivalent circuit of a single –phase induction machine.

[10 Marks]